## Slide 1: Instruction Queue
 8086 employs parallel processing
 When EU is busy decoding or executing current instruction, the buses of 8086 may not be in use.
 At that time, BIU can use buses to fetch upto six instruction bytes for the following instructions
 BIU stores these pre-fetched bytes in a FIFO register called Instruction Queue
 When EU is ready for its next instruction, it simply reads the instruction from the queue in BIU
1

## Slide 2: Pipelining
EU of 8086 does not have to wait in between for BIU to fetch next instruction byte from memory
So the presence of a queue in 8086 speeds up the processing
Fetching the next instruction while the current instruction executes is called pipelining
2

## Slide 3: Memory Segmentation
 8086 has a 20-bit address bus
 So it can address a maximum of 1MB of memory
 8086 can work with only four 64KB segments at a time within this 1MB range
 These four memory segments are called
• Code segment
• Stack segment
• Data segment
• Extra segment
3

## Slide 4: Memory
4
5
6
7
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
00000H
FFFFFH
1MB
Address Range
64KB Memory Segment
Only 4 such segments can be addressed at a time
4

## Slide 5
5
Code Segment
 That part of memory from where BIU is currently fetching instruction code bytes
Stack Segment
 A section of memory set aside to store addresses and data while a subprogram executes
Data & Extra Segments
 Used for storing data values to be used in the program

## Slide 6: Memory
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
00000H
FFFFFH
1MB
Address Range
Code Segment
Stack Segment
Data & Extra Segments
6

## Slide 7: Segment Registers
hold the upper 16-bits of the starting address for each of the segments
The four segment registers are
• CS (Code Segment register)
• DS (Data Segment register)
• SS (Stack Segment register)
• ES (Extra Segment register)
7

## Slide 8: Memory
1
Code Segment
3
4
Data Segment
Extra Segment
7
8
9
10
11
12
13
14
15
Stack Segment
00000H
FFFFFH
1MB
Address Range
Starting Addresses
of Segments
8
1000
0H
4000
0H
0H
5000
F000
0H
CS
DS ES
SS

## Slide 9
Address of a segment is of 20-bits
A segment register stores only upper 16- bits
BIU always inserts zeros for the lowest 4- bits of the 20-bit starting address.
E.g. if CS = 348AH, then the code segment will start at 348A0H
A 64-KB segment can be located anywhere in the memory, but will start at an address with zeros in the lowest 4-bits
9

## Slide 10: Instruction Pointer (IP) Register
a 16-bit register
Holds 16-bit offset, of the next instruction byte in the code segment
BIU uses IP and CS registers to generate the 20-bit address of the instruction to be fetched from memory
10

## Slide 11: Physical Address Calculation
1
Data Segment
3
4
Code Segment
Extra Segment
7
8
9
10
11
12
13
14
15
Stack Segment
Memory
00000H
1MB
Address Range
348A0 H
+ 4214 H
38AB4 H
CS
IP
Physical Address
MOV AL, BL
Start of Code Segment
348A0H
IP = 4214H
Code Byte
38AB4H
FFFFF72H

## Slide 12
Stack Segment (SS) Register Stack Pointer (SP) Register
Upper 16-bits of the starting address of stack segment is stored in SS register
It is located in BIU
SP register holds a 16-bit offset from the start of stack segment to the top of the stack
It is located in EU
12

## Slide 13: Other Pointer & Index Registers
Base Pointer (BP) register
Source Index (SI) register
Destination Index (DI) register
Can be used for temporary storage of data
Main use is to hold a 16-bit offset of a data word in one of the segments
13

## Slide 14: ADDRESSING MODES OF 8086
14

## Slide 15: Various Addressing Modes
1. Immediate Addressing Mode
2. Register Addressing Mode
3. Direct Addressing Mode
4. Register Indirect Addressing Mode
5. Index Addressing Mode
6. Based Addressing Mode
7. Based & Indexed Addressing Mode
8. Based & Indexed with displacement Addressing Mode
9. Strings Addressing Mode
76
Presented by C.GOKUL,AP/EEE , Velalar College of Engg & Tech, Erode

## Slide 16: 1. IMMEDIATE ADDRESSING MODE
16
• The instruction will specify the name of the register which holds the data to be operated by the instruction.
• Source data is within the instruction
• Ex: MOV AX,10ABH
 AL=ABH,
AH=10H

## Slide 17: 2.REGISTER ADDRESSING MODE
17
• In immediate addressing mode, an 8-bit or 16-bit data is specified as part of the instruction
• Ex: MOV AX,BLH MOV AX,BLH

## Slide 18: 3. DIRECT ADDRESSING MODE
• Memory address is supplied with in the instruction
• Mnemonic: MOV AH,[MEMBDS] AH [1000H]
• But the memory address is not
index or pointer register
18

## Slide 19: 4. REGISTER INDIRECT ADDRESSING MODE
• Memory address is supplied in an index or pointer register
• EX:
MOV AX,[SI] ;
JMP [DI] ;
AL [SI] ; AH [SI+1] IP [DI+1: DI]
INC BYTE PTR [BP] ; [BP] DEC WORD PTR [BX] ;
[BX+1:BX]
[BP]+1
[BX+1:BX]-1
19

## Slide 20: 5.Indexed Addressing Mode
• Memory address is the sum of index register plus displacement
MOV AX,[SI+2] AL [SI+2]; AH [SI+3] JMP [DI+2] IP [BX+3:BX+2]
20

## Slide 21: 6. Based Addressing Mode
• Memory address is the sum of the BX or BP base register plus a displacement within instruction
• Ex:
MOV AX,[BP+2] AL [BP+2]; AH [BP+3] JMP [BX+2] IP [BX+3:BX+2]
21

## Slide 22: 7.BASED & INDEX ADDRESSING MODES
• Memory address is the sum of the index register & base register
Ex:
MOV AX,[BX+SI] ; AL [BX+SI] ; AH JMP [BX+DI] ; IP
[BX+SI+1]
[BX+DI+1 : BX+DI]
INC BYTE PTR [BP+SI] ; [BP]
[BP]+1
DEC WORD PTR [BP+DI] ;
[BX+1:BX]
[BX+1:BX]-1
22

## Slide 23: 8. BASED & INDEXED WITH DISPLACEMENT ADDRESSING MODE
• Memory address is the sum of an index register , base register and displacement within instruction
MOV AX,[BX+SI+6] ; AL [BX+SI+6] ; AH
JMP [BX+DI+6] ; IP
[BX+SI+7]
[BX+DI+7 : BX+DI+6]
INC BYTE PTR [BP+SI+5] ; DEC WORD PTR [BP+DI+5] ;
Presented by C.GOKUL,AP/EEE , Velalar College of Engg & Tech, Erode
23

## Slide 24: 9. Strings Addressing Mode
• The memory source address is a register SI in the data segment, and the memory destination address is register DI in the extra segment
• Ex: MOVSB [ES:DI] [DS:SI]
• If DF=0 SI
DF=1 SI
SI+1 SI-1
, DI DI+1
, DI DI-1
24

## Slide 25: INSTRUCTION SET of 8086
25

## Slide 26: Instruction set basics
• Instruction:- An instruction is a binary pattern designed inside a microprocessor to perform a specific function.
• Opcode:- It stands for operational code. It specifies the type of operation to be performed by CPU. It is the first field in the machine language instruction format.
• E.g. 08 is the opcode for instruction “MOV X,Y”.
• Operand:- We can also say it as data on which operation should act. operands may be register values or memory values. The CPU executes the instructions using information present in this field. It may be 8-bit data or 16-bit data.
26

## Slide 27: Instruction set basics
• Assembler:- it converts the instruction into sequence of binary bits, so that this bits can be read by the processor.
• Mnemonics:- these are the symbolic codes for either instructions or commands to perform a particular function.
• E.g. MOV, ADD, SUB etc.
27

## Slide 28: Types of instruction set of 8086 microprocessor (1). Data Copy/Transfer instructions.
28
(2). Arithmetic & Logical instructions.
(3). Branch instructions.
(4). Loop instructions.
(5). Machine Control instructions. (6). Flag Manipulation instructions. (7). Shift & Rotate instructions. (8). String instructions.

## Slide 29: (1). Data copy/transfer instructions.
29
(1). MOV Destination, Source
⚫ There will be transfer of data from source to destination.
⚫ Source can be register, memory location or immediate data.
⚫ Destination can be register or memory operand.
⚫ Both Source and Destination cannot be memory location or segment registers at the same time.
⚫ E.g.
⚫ (1). MOV CX, 037A H;
⚫ (2). MOV AL, BL;
⚫ (3). MOV BX, [0301 H];

## Slide 30: BEFORE EXECUTION
BX | 2000H
30
AX | 2000H
AFTER EXECUTION
MOV BX,AX
A H |  | AL | 
B H |  | BL | 
C H |  | CL | 
D H |  | DL | 
A H |  | AL | 
B H |  | BL | 
C H |  | CL | 40
D H |  | DL | 
MOV CL,M
40
40
BEFORE EXECUTION
AFTER EXECUTION

## Slide 31: Stack Pointer
31
⚫ It is a 16-bit register, contains the address of the data item currently on top of the stack.
⚫ Stack operation includes pushing (providing) data on to the stack and popping (taking)data from the stack.
⚫ Pushing operation decrements stack pointer and Popping operation increments stack pointer. i.e. there is a last in first out (LIFO) operation.

## Slide 32: (2). Push Source
32
⚫ Source can be register, segment register or memory.
⚫ This instruction pushes the contents of specified source on to the stack.
⚫ In this stack pointer is decremented by 2.
⚫ The higher byte data is pushed first (SP-1).
⚫ Then lower byte data is pushed (SP-2).
⚫ E.g.:
⚫ (1). PUSH AX;
⚫ (2). PUSH DS;
⚫ (3). PUSH [5000H];

## Slide 33
INITIAL POSITION
DECREMENTS SP & STORES HIGHER BYTE
HIGHER BYTE
DECREMENTS SP & STORES LOWER BYTE
LOWER BYTE
HIGHER BYTE
(1) STACK POINTER
(2) STACK POINTER
(3) STACK POINTER
33

## Slide 34: BEFORE EXECUTION
34
50
10
SP | 2002H |  | 
BH |  | BL | 
CH | 10 | CL | 50
DH |  | DL | 
SP | 2000H |  | 
BH |  | BL | 
CH | 10 | CL | 50
DH |  | DL | 
2000H
2001H
2002H
2000H
2001H
2002H
PUSH CX
AFTER EXECUTION

## Slide 35: (3) POP Destination
35
⚫ Destination can be register, segment register or memory.
⚫ This instruction pops (takes) the contents of specified destination.
⚫ In this stack pointer is incremented by 2.
⚫ The lower byte data is popped first (SP+1).
⚫ Then higher byte data is popped (SP+2).
⚫ E.g.
⚫ (1). POP AX;
⚫ (2). POP DS;
⚫ (3). POP [5000H];

## Slide 36: (1) STACK POINTER
INITIAL POSITION AND READS LOWER BYTE
LOWER BYTE
INCREMENTS SP & READS HIGHER BYTE
LOWER BYTE
HIGHER BYTE
INCREMENTS SP
LOWER BYTE
HIGHER BYTE
(2) STACK POINTER
(3) STACK POINTER
36

## Slide 37: BEFORE EXECUTION
SP | 2000H |  | 
BH |  | BL | 
37
SP | 2002H |  | 
BH | 5 0 | BL | 30
30
50
30
50
AFTER EXECUTION
POP BX
2000H
2001H
2002H
2000H
2001H
2002H

## Slide 38: (4). XCHG Destination, source;
38
• This instruction exchanges contents of Source with destination.
• It cannot exchange two memory locations directly.
•The contents of AL are exchanged with BL.
•The contents of AH are exchanged with BH.
•E.g.
(1). XCHG BX, AX;
(2). XCHG [5000H],AX;

## Slide 39: AFTER EXECUTION
AH | 20 | AL | 40
BH | 70 | BL | 80
39
AH | 70 | AL | 80
BH | 20 | BL | 40
BEFORE EXECUTION
XCHG AX,BX

## Slide 40: (5)IN AL/AX, 8-bit/16-bit port address
40
⚫ It reads from the specified port address.
⚫ It copies data to accumulator from a port with 8- bit or 16-bit address.
⚫ DX is the only register is allowed to carry port address.
⚫ E.g.
(1). IN AL, 80H;
(2). IN AX,DX; //DX contains address of 16-bit port.

## Slide 41: BEFORE EXECUTION
10
AL
10
41
AL | 10
IN AL,80H
AFTER EXECUTION
PORT 80H
PORT 80H

## Slide 42: OUT 8-bit/16-bit port address, AL/AX
42
⚫ It writes to the specified port address.
⚫ It copies contents of accumulator to the port with 8-bit or 16-bit address.
⚫ DX is the only register is allowed to carry port address.
⚫ E.g.
(1). OUT 80H,AL;
(2). OUT DX,AX; //DX contains address of 16-bit port.

## Slide 43: BEFORE EXECUTION
10
AL | 40
40
43
AL | 40
OUT 50H,AL
AFTER EXECUTION
PORT 50H
PORT 50H

## Slide 44: (7) XLAT
44
⚫ Also known as translate instruction.
⚫ It is used to find out codes in case of code conversion.
⚫ i.e. it translates code of the key pressed to the corresponding 7-segment code.
⚫ After execution this instruction contents of AL register always gets replaced.
⚫ E.g. XLAT;

## Slide 45
8.LEA 16-bit register (source), address (dest.)
⚫ LEA Also known as Load Effective Address (LEA).
⚫ It loads effective address formed by the destination into the source register.
⚫ E.g.
(1). LEA BX,Address;
(2). LEA SI,Address[BX];
45

## Slide 46: (9). LDS 16-bit register (source), address (dest.); (10). LES 16-bit register (source), address (dest.);
46
⚫ LDS Also known as Load Data Segment (LDS).
⚫ LES Also known as Load Extra Segment (LES).
⚫ It loads the contents of DS (Data Segment) or ES (Extra Segment) & contents of the destination to the contents of source register.
⚫ E.g.
(1). LDS BX,5000H;
(2). LES BX,5000H;

## Slide 47: (1). LDS BX,5000H; (2). LES BX,5000H;
10
20
30
40
5000H
5001H
5002H
5003H
20 | 10
40 | 30
47
BX
DS/ES
7 0
0
15

## Slide 48
(11). LAHF:- This instruction loads the AH register from the contents of lower byte of the flag register.
⚫ This command is used to observe the status of the all conditional flags of flag register.
E.g. LAHF;
(12). SAHF:- This instruction sets or resets all conditional flags of flag register with respect to the corresponding bit positions.
⚫ If bit position in AH is 1 then related flag is set otherwise flag will be reset.
E.g. SAHF;
48

## Slide 49: PUSH & POP
49
(13). PUSH F:- This instruction decrements the stack pointer by 2.
⚫ It copies contents of flag register to the memory location pointed by stack pointer.
⚫ E.g. PUSH F;
(14). POP F:- This instruction increments the stack pointer by 2.
⚫ It copies contents of memory location pointed by stack pointer to the flag register.
⚫ E.g. POP F;

## Slide 50: (2). Arithmetic Instructions
50
⚫ These instructions perform the operations like:
⚫ Addition,
⚫ Subtraction,
⚫ Increment,
⚫ Decrement.

## Slide 51: (2). Arithmetic Instructions (1). ADD destination, source;
51
⚫ This instruction adds the contents of source operand with the contents of destination operand.
⚫ The source may be immediate data, memory location or register.
⚫ The destination may be memory location or register.
⚫ The result is stored in destination operand.
⚫ AX is the default destination register.
⚫ E.g. (1). ADD AX,2020H;
(2). ADD AX,BX;

## Slide 52
AH | 10 | AL | 10
AFTER EXECUTION
BEFORE EXECUTION
AH | 10 | AL | 10
BH | 20 | BL | 20
AFTER EXECUTION
BEFORE EXECUTION
ADD AX,BX
AH | 30 | AL | 30
ADD AX,2020H
1010
+2020
3030
AH | 30 | AL | 30
BH | 20 | BL | 20
52

## Slide 53: ADC destination, source
53
⚫ This instruction adds the contents of source operand with the contents of destination operand with carry flag bit.
⚫ The source may be immediate data, memory location or register.
⚫ The destination may be memory location or register.
⚫ The result is stored in destination operand.
⚫ AX is the default destination register.
⚫ E.g. (1). ADC AX,2020H;
(2). ADC AX,BX;

## Slide 54: (3) INC source
54
⚫ This instruction increases the contents of source operand by 1.
⚫ The source may be memory location or register.
⚫ The source can not be immediate data.
⚫ The result is stored in the same place.
⚫ E.g. (1). INC AX;
(2). INC [5000H];

## Slide 55
AFTER EXECUTION
5000H
AFTER EXECUTION
BEFORE EXECUTION
INC [5000H]
BEFORE EXECUTION
INC AX
AH | 10 | AL | 11
AH | 10 | AL | 12
1011
5000H
1012
55

## Slide 56: 4. DEC source
56
⚫ This instruction decreases the contents of source operand by 1.
⚫ The source may be memory location or register.
⚫ The source can not be immediate data.
⚫ The result is stored in the same place.
⚫ E.g. (1). DEC AX;
(2). DEC [5000H];

## Slide 57: DEC AX
AFTER EXECUTION
5000H
AFTER EXECUTION
BEFORE EXECUTION
DEC [5000H]
BEFORE EXECUTION
AH | 10 | AL | 11
AH | 10 | AL | 10
1051
5000H
1050
57

## Slide 58: (5) SUB destination, source;
58
⚫ This instruction subtracts the contents of source operand from contents of destination.
⚫ The source may be immediate data, memory location or register.
⚫ The destination may be memory location or register.
⚫ The result is stored in the destination place.
⚫ E.g. (1). SUB AX,1000H;
(2). SUB AX,BX;

## Slide 59: BEFORE EXECUTION
AFTER EXECUTION
AFTER EXECUTION
BEFORE EXECUTION
SUB AX,BX
AH | 20 | AL | 00
AH | 10 | AL | 00
SUB AX,1000H
2000
-1000
=1000
AH | 20 | AL | 00
BH | 10 | BL | 00
59
AH | 10 | AL | 00
BH | 10 | BL | 00

## Slide 60: (6). SBB destination, source;
60
⚫ Also known as Subtract with Borrow.
⚫ This instruction subtracts the contents of source operand & borrow from contents of destination operand.
⚫ The source may be immediate data, memory location or register.
⚫ The destination may be memory location or register.
⚫ The result is stored in the destination place.
⚫ E.g. (1). SBB AX,1000H;
(2). SBB AX,BX;

## Slide 61: BEFORE EXECUTION AFTER EXECUTION
AFTER EXECUTION
BEFORE EXECUTION
SBB AX,1000H
SBB AX,BX
2050
AH | 10 | AL | 19
2020
- 1000
1020-
1=1019
AH | 10 | AL | 19
BH | 10 | BL | 10
61
B | 1 |  |  |  | 
AH |  | 20 |  | AL | 20
B | 1 |  |  |  | 
AH |  | 20 |  | AL | 20
BH |  | 10 |  | BL | 10

## Slide 62: (7). CMP destination, source
62
⚫ Also known as Compare.
⚫ This instruction compares the contents of source operand with the contents of destination operands.
⚫ The source may be immediate data, memory location or register.
⚫ The destination may be memory location or register.
⚫ Then resulting carry & zero flag will be set or reset.
⚫ E.g. (1). CMP AX,1000H;
(2). CMP AX,BX;

## Slide 63: BEFORE EXECUTION
AFTER EXECUTION
63
CMP AX,BX
CY | 0 | Z | 1
AFTER EXECUTION
BEFORE EXECUTION
D=S: CY=0,Z=1 D>S: CY=0,Z=0 D<S: CY=1,Z=0
AH | 10 | AL | 00
BH | 10 | BL | 00
CMP AX,BX
CY | 0 | Z | 0
AH | 10 | AL | 00
BH | 00 | BL | 10
AFTER EXECUTION
BEFORE EXECUTION
CMP AX,BX
CY | 1 | Z | 0
AH | 10 | AL | 00
BH | 20 | BL | 00

## Slide 64
⚫ AAA (ASCII Adjust after Addition):
⚫ The data entered from the terminal is in ASCII format.
⚫ In ASCII, 0 – 9 are represented by 30H – 39H.
⚫ This instruction allows us to add the ASCII codes.
⚫ This instruction does not have any operand.
⚫ Other ASCII Instructions:
⚫ AAS (ASCII Adjust after Subtraction)
⚫ AAM (ASCII Adjust after Multiplication)
⚫ AAD (ASCII Adjust Before Division)
64

## Slide 65
⚫ DAA (Decimal Adjust after Addition)
⚫ It is used to make sure that the result of adding two BCD numbers is adjusted to be a correct BCD number.
⚫ It only works on AL register.
⚫ DAS (Decimal Adjust after Subtraction)
⚫ It is used to make sure that the result of subtracting two BCD numbers is adjusted to be a correct BCD number.
⚫ It only works on AL register.
65

## Slide 66: MUL operand
66
⚫ Unsigned Multiplication.
⚫ Operand contents are positively signed.
⚫ Operand may be general purpose register or memory location.
⚫ If operand is of 8-bit then multiply it with contents of AL.
⚫ If operand is of 16-bit then multiply it with contents of AX.
⚫ Result is stored in accumulator (AX).
⚫ E.g. (1). MUL BH
⚫
(2). MUL CX
// AX= AL*BH; // (+3) * (+4) = +12.
// AX=AX*CX;

## Slide 67: IMUL operand
67
⚫ Signed Multiplication.
⚫ Operand contents are negatively signed.
⚫ Operand may be general purpose register, memory location or index register.
⚫ If operand is of 8-bit then multiply it with contents of AL.
⚫ If operand is of 16-bit then multiply it with contents of AX.
⚫ Result is stored in accumulator (AX).
⚫ E.g. (1). IMUL BH
// (-3) * (-4) = 12.
⚫
(2). IMUL CX
// AX= AL*BH;
// AX=AX*CX;

## Slide 68: DIV operand
68
⚫ Unsigned Division.
⚫ Operand may be register or memory.
⚫ Operand contents are positively signed.
⚫ Operand may be general purpose register or memory location.
⚫ AL=AX/Operand (8-bit/16-bit) & AH=Remainder.
⚫ E.g. | MOV AX, 0203 | // AX=0203
⚫ | MOV BL, 04 | // BL=04
⚫ | IDIV BL | // AL=0203/04=50 (i.e. AL=50 & AH=03)

## Slide 69: IDIV operand
69
⚫ Signed Division.
⚫ Operand may be register or memory.
⚫ Operand contents are negatively signed.
⚫ Operand may be general purpose register or memory location.
⚫ AL=AX/Operand (8-bit/16-bit) & AH=Remainder.
⚫ E.g.
MOV AX, -0203
MOV BL, 04
⚫
⚫
DIV BL
// AX=-0203
// BL=04
// AL=-0203/04=-50 (i.e. AL=-50 &
AH=03)

## Slide 70: Multiplication and Division Examples
70

## Slide 71: BEFORE EXECUTION
AH | 00 | AL | 05
BH | 00 | BL | 03
CH |  | CL | 
71
AFTER EXECUTION
MUL BX
AX=lower 16 bit {000F} DX=Higher 16 bit {0000}
AH | 00 | AL | 0F
BH |  | BL | 
CH |  | CL | 
DH | 00 | DL | 00
0005*0003 = 0000 000F

## Slide 72: BEFORE EXECUTION
AH | 00 | AL | 0F
BH | 00 | BL | 02
CH |  | CL | 
AFTER EXECUTION
DIV BX
AH | 00 | AL | 07
BH |  | BL | 
CH |  | CL | 
DH | 00 | DL | 01
AX=Quotient {0007}
DX=Reminder {0001}
000F = 7 1
0002
2
72

## Slide 73
73

## Slide 74
74